## Slide 1: Building daily CalLite model from scratch – daily version

## Slide 2: Goals
Learn how to rebuild CalLite schematic North of Delta model from scratch using daily data
  Including Delta operations and requirements will be saved for later
Review how WRESL routes water without actual channel routing like Muskingum method
Determine the validity and corroborate the results

## Slide 3: North of Delta Daily 1-year model
Time period
  August 2019-August 2020 (mostly water year 2020)
Progresses as phases and sub-phases which can be done on parallel paths
  Feather River to Confluence
  Yuba River to Confluence
  Feather-Yuba to SacFeather confluence
  Shasta to Red Bluff
  Trinity to Red Bluff
  Shasta-Trinity to SacFeather confluence

## Slide 4: Schematic

## Slide 5: Questons
What is the philosophy of using Accretion-Depletion (AD) terms?
How to estimate daily AD terms from available daily data?
  Is it okay to estimate these terms using CDEC data or will I have to refer to CalSim II data?
With the

## Slide 6: AD_KSWCK
Three components
  Shasta dam (SHA) release
  Inflow from Spring Creek (SPC)
  Keswick dam release (KES)

## Slide 7: Connaughton (2014)
Sacramento Valley Integrated Reservoir Optimization Model (SVIROM): Flood Control linear program
Provided appendix with derived Muskingum routing coefficients
Reach 16 would be

## Slide 8: CalLite schematic

## Slide 9: Phase 1 data requirements
Lake Oroville
  Inflow (TAF/day)
  Initial storage
  Level 5 storage
  Evaporation rate
Oroville water rights demands
Minimum groundwater pumping

## Slide 10: Thermalito demands and diversions
Region | Delivery Node | Project Delivery Type | 
Western Canal | D7A_PWR | Water rights | 
 | D7A_PAG | Agricultural | 
 | D7A_PRF | Refuge | 
Joint Canal | D7B_PWR | Water rights | 
 | D7B_PAG | Agricultural | 
 | D7B_PRF | Refuge | 
Rice decomp | D7C |  | 
Butte County | D201_PIMI | Indoor M&I | 
 | D201_POMI | Outdoor M&I | 
Thermalito Irrigation District | D202_PWR | Water rights |