## Slide 1: Building daily CalLite model from scratch – daily version

## Slide 2: Goals
Learn how to rebuild CalLite schematic North of Delta model from scratch using daily data
  Including Delta operations and requirements will be saved for later
Review how WRESL routes water without actual channel routing like Muskingum method
Determine the validity and corroborate the results

## Slide 3: North of Delta Daily 1-year model
Time period
  August 2019-August 2020 (mostly water year 2020)
Progresses as phases and sub-phases which can be done on parallel paths
  Feather River to Confluence
  Yuba River to Confluence
  Feather-Yuba to SacFeather confluence
  Shasta to Red Bluff
  Trinity to Red Bluff
  Shasta-Trinity to SacFeather confluence

## Slide 4: Schematic

## Slide 5: Phase 1.1 – Oroville dam and outflow only
Develop very simple model
  Inflow to Oroville reservoir
  Oroville reservoir storage
  Release from Oroville storage
  No deliveries/demands yet
Output
  Daily Oroville releases

## Slide 6: Phase 1.2 – Include Oroville deliveries
Include D_OROVL missing from previous step
Output
  Oroville releases, storage, deliveries

## Slide 7: Phase 1.3 – Include Thermalito node
No deliveries yet
Just the passing of water from C_OROVL to C_THERM
Need to review the purpose of Accretion-Depletion (AD) terms and how to calculate
Output
  Flow from Thermalito (C_THERM)

## Slide 8: Phase 1.4 – Include Thermalito deliveries
Add demands for D_THERM
Need to review the purpose of Accretion-Depletion (AD) terms and how to calculate
Output
  D_THERM

## Slide 9: Phase 1 data requirements
Lake Oroville
  Inflow (TAF/day)
  Initial storage
  Level 5 storage
  Evaporation rate
Oroville water rights demands
Minimum groundwater pumping

## Slide 10: Phase 2.1 – Shasta dam and outflow only
Develop very simple model
  Inflow to Shasta reservoir
  Shasta reservoir storage
  Release from Shasta storage
Output
  Daily Shasta releases